## Slide 1
Automatic Program Loading in Unison
An Amkor Requirement for Automation (v 2.11.20191105)

## Slide 2: Overview

## Slide 3: What Factory Automation Does Amkor Require From Testers?
Loading Test Programs
  Operators don’t load test programs manually through tester interface
  A remote server sends a text file, typically named “lotinfo.txt” that contains Test program name and location, Lot ID, Step field (refers to test type, e.g. Retest, QA test, ), Temperature.
  Tester to load the test program specified in the “lotinfo.txt” file as soon as it receives it.
Set STDF header field values
  “lotinfo.txt” files may also contain data that Amkor wants to set to STDF fields, specifically MIR and SDR records.
  Tester is expected to send these data to Unison to set them in STDF file
Real-time monitoring (Bin Solution)
  For ever test cycle, tester must send per-site binning as string in packets of bytes to remote server
  Tester must be capable of connecting to Amkor’s network and send this packets of bytes

## Slide 4: What COHU Needs to Provide to Meet Amkor Requirement?
Tester must be able to monitor incoming “lotinfo.txt” files from a server in real-time
Tester must be able to parse the contents of “lotinfo.txt” file
Tester must be able to automatically load test program specified In “lotinfo.txt” file in Unison interface
Tester must be able to set STDF fields taken from “lotinfo.txt” into Unison
Tester must have the capability to connect to remote server (e.g. through socket) and be able to send packet of bytes

## Slide 5: Problem
Unison does not have the ability to monitor incoming files from remote server
Unison does not have the ability to parse text files
Unison interface (OICU and Optool) can only load programs manually by default
Unison can set STDF fields but it has to be done within test program
  An interface is needed to send the data from “lotinfo.txt” file to test program
Unison does not have the ability to connect to network and send packets of data to a remote server

## Slide 6: Solution: Automatic Program Loader (APL)
To develop a software that can do the following
  Monitor incoming files from server at a specified location in the tester
  Parse “lotinfo.txt” file
  Launch Unison Interface (OICU or Optool)
  Load test program specified in “lotinfo.txt” file upon receiving it
  Send data from “lotinfo.txt” file to Unison as STDF field values
  Be able to connect via socket to a remote server and send bytes of data containing bin results in real-time
This software must be stand alone and can run in the background within the tester

## Slide 7: Implementation: Software Design
There are 4 components in the APL software
  APL exec
  APL Commander (GUI Engine)
  FAModule
  Custom Datalog Application
APL exec
  The main component of APL
  Monitor incoming “Lotinfo.txt” file and parse it
  Launch Unison interface and load test program automatically
  Send STDF fields to Unison
  Connect to network and send bin information for every test cycle
FAModule (optional)
  Certain STDF fields must be taken from handler or prober.
Custom Datalog Application (optional)
  Certain STDF fields are not possible to set outside of Unison (e.g. GDR, PTR) therefore APL exec and FAModule will not be able to do it
  Amkor requires Unison to generate custom summary file and to this can be implemented in this application. This feature is currently under development
APL Commander
  Runs along side APL exec as a separate thread handling GUI like warning messages, Operator Prompts.
  Can be used to send command to APL. This feature is not available yet but will be in future version release if a requirement arises

## Slide 8: Implementation: Technologies Used
EVXA
  A Unison C++ library used as a bridge in order for APL exec to talk and exchange data/states with Unison
  Used to launch Unison, load and unload program, send STDF fields, etc…
Inotify
  A linux C++ library used to monitor incoming, outgoing, and file creation within directories in CentOS
  Used to monitor incoming “lotinfo.txt” file
wxWidgets 3.0.4
  An open source, cross platform C++ library used to create GUI application
Linux built-in C++ socket library
  A standard C/C++ library used to connect to remote server via socket
  Used for sending bin information per test cycle
The following functions are developed from ground up to achieve capability
  “Lotinfo.txt” file parser. This file is in YAML format
  XML file parser. APL has a lot functions that you can turn ON or OFF or set its parameters. These functions can be configured through an XML file, much like CURI

## Slide 9: Status: Where We Are Right Now With APL?
APL is now operational and currently running in Amkor factory
The latest version is in beta b.2.11.20191105
It can now perform the following
  Monitoring incoming “lotinfo.txt” file and parse it
  Launch OICU or Optool if necessary
  Load test program
  Send STDF data specified in “lotinfo.txt” to Unison
  Send binning information per test cycle to remote server (Amkor Bin Solution v1.4 compliant)
  Safely loads program when existing program is already loaded in Unison (Operator GUI Prompts)
  Can be configured on how to parse lotinfo.txt contents
For PAx tester and Qualcomm devices, FAModule is not required for now
Custom Datalog Applications is currently under development to implement custom summary, an Amkor requirement.

## Slide 10: Status: To-Do list
Custom Datalog Applications is currently under development to implement custom summary, an Amkor requirement.
Enable APL on DMDx/ST on Wafer Test; Amkor currently observing performance on DMDx/FT setup before deciding on enabling in Wafer Test.

## Slide 11: Technical Details

## Slide 12: Installation
Where to download/copy APL
  Kindly contact allan.asis@cohu.com for a link to download a copy of APL
How to install
  To unpack the file use the command >tar –xzvf APL.tar.gz
  Optionally, you can call ‘make apl_exec’ command inside APL folder after you unpack it so it gets compiled
    Note that ‘make’ will not work as there will be compiler error. Make sure it’s ‘make apl_exec’ as specified

## Slide 13: Configuration
APL software is packed with features and thus require a lot of knobs and switches to control them
  These features can either be enabled or disabled.
  Some features can also be configured to behave the way you want it
  Some features require parameters to work
APL reads a configuration file containing parameters that specifies how features work or behave.
What is this configuration file?
  A text file written in XML format, just like CURI config
  Filename can be anything and be located anywhere in the tester PC
What features can be controlled in configuration file?
  Operator Interface tester will use
  filename and directory of the file coming from server that contains test program to load
  Binning solution
  socket connection
  STDF writing
  Miscellaneous behaviors e.g. load program time-out
  And more…

## Slide 14: Configuration File
An example of what’s inside a configuration file look like. Tags are case sensitive.
  <?xml version="1.0" encoding="UTF-8"?>
  <APL_CONF>
  <CurrentSiteConfiguration>Singapore</CurrentSiteConfiguration>
  <SiteConfiguration name = "Singapore">
  <Launch/>
  <Summary state = “false
  <LotInfo>
  <File>b.txt</File> <!-- default: lotinfo.txt -->
  <Path>/home/localuser/Desktop/APL</Path> <!-- default: /tmp -->
  </LotInfo>
  <Binning state = "true">
  <SocketType>udp</SocketType>
  <IP>127.0.0.1</IP>
  <Port>4000</Port>
  </Binning>
  <Logging state = “false“/>
  <STDF state = "true" />
  <FAMODULE state = "true" />
  </SiteConfiguration>
  </APL_CONF>

## Slide 15: Configuration File: Root Elements
The first line is a prolog that defines the XML version and character encoding
  <?xml version="1.0" encoding="UTF-8"?>
The next line <APL_CONF> is the <root> element.
  All parameters must be branched within this tag
  This tag allows APL parsers to identify this file as a valid configuration file
  It contains two branches
    <CurrentSiteConfiguration>
    <SiteConfiguration>

## Slide 16: Configuration File: Active Configuration
<SiteConfiguration>
  This tag contains the configuration parameters
  The file can contain multiple <SiteConfiguration> each uniquely identified with their “name” attribute
<CurrentSiteConfiguration>
  Although the file can contain multiple <SiteConfiguration>, there can only be one active. This tag points to the active configuration
An example with multiple configuration file and one of them as active
  <APL_CONF>
  <CurrentSiteConfiguration>Singapore</CurrentSiteConfiguration>
  <SiteConfiguration name = "Singapore“/>
  <SiteConfiguration name = “Amkor“/>
  <SiteConfiguration name = “Debug“/>
  </APL_CONF>

## Slide 17: Configuration File: Site Configuration Parameters
<SiteConfiguration> can contain the following tags
  <Launch>
    Control how Unison is launched as well as how program is loaded.
    Tester, Factory and hardware information are also set
  <LotInfo>
    Specify the “lotinfot.txt” file from remote server that contains test program to be loaded and optional STDF parameters
    Configure how APL will parse “lotinfo.txt” file
  <Binning>
    Configure how APL will send binning information to remote server, a feature that supports Amkor’s binning solution
  <Logging>
    Configure APL’s logging mechanism
  <STDF>
    Option to send data from “lotinfot.txt” file to STDF file
    Option to let APL rename STDF file to meet Qualcomm specification
  <FAMODULE>
    Option to send “lotinfo.txt” file to FAModule (if it is running) and parse it

## Slide 18: Configuration File: Launch Parameters
< Launch > can contain the following tags (Note that Param name is case sensitive but the values are not)
  <Param name = "Type">prod</Param>
    Specifies the type of interface to be launched.
    Set to “prod” to launch OICU or “engr” to launch OpTool
    Default is “prod”
  <Param name = "Kill Tester Before Launch">false</Param>
    If true, APL will attempt to kill Unison if there’s currently one running and launch Unison again to load program
    Default is false
  <Param name = "Wait Time To Launch">120</Param>
    After APL launches Unison, it will wait at specified time (in seconds) set in this parameter before it decides to try again.
    Default is 120 seconds
  <Param name = "Max Attempt To Launch">3</Param>
    The number of times APL will attempt to launch Unison before it reports an error
    Default is 3
  <Param name = "Wait Time To End Lot">20</Param>
    Before APL loads program, it will check first if an existing program is loaded and currently testing a lot. It will attempt to end the lot before unloading the existing program. This is the wait time APL will wait before Unison ends the lot. If this expires, APL will proceed in unloading current program
    Default is 30 seconds

## Slide 19: Configuration File: Launch Parameters
More < Launch > tags…
  <Param name = "Wait Time To Unload Program">20</Param>
    APL will unload existing program before loading the new one. After it attempts to unload the current program, it will wait for Unison to confirm that the program has unloaded. APL will not wait forever. Instead it will wait until the time specified set in this parameter
    Default is 30 seconds
  <Param name = "Wait Time To FAModule">20</Param>
    If <FAMODULE> parameter is enabled, APL will wait for FA Module to finish processing the “lotinfo.txt” file.
  <Param name = "Wait Time To Kill Tester">30</Param>
    If APL has to kill Unison before it launches a new one, it will wait until the time specified in this parameter expires.
    Default is 30 seconds
  <Param name = "Force Load">true</Param>
    By default, APL will not load new program if the same program is already loaded. If this parameter is set to “true”, APL will always unload existing program even if it’s the same program
    Default is false
  <Param name = "NewLot Config Path">/home/test/PROD/qctpax/Desktop/APL</Param>
    OICU’s New Lot UI Dialog Box can be customized through this file. Specify the path where this file is located
  <Param name = "NewLot Config File">NewLotUnison</Param>
    OICU’s New Lot UI Dialog Box can be customized through this file. Specify the name of this file

## Slide 20: Configuration File: Launch Parameters
More < Launch > tags…
  <Param name = "Test Site">AMKKR3-S</Param>
    This field specifies the test site for which APL is running. This is used as one of the parameters in Qualcomm’s STDF filename format
  <Param name = "Supplier">AMKOR</Param>
    This field specifies the factory for which APL is running. This is used as one of the parameters in Qualcomm’s STDF filename format

## Slide 21: Configuration File: LotInfo Parameters
< LotInfo > can contain the following tags (Note that Param name is case sensitive but the values are not)
  <File>lotinfo.txt</File>
    Specifies the expected filename of the “lotinfo.txt” that will be received from server
    Default is lotinfo.txt
  <Path>/home/localuser/Desktop/APL</Path>
    Specifies the path APL will wait for incoming “lotinfo.txt” file
    Default is “/tmp”
  <Delete>false</Delete>
    By default, APL will not delete the “lotinfo.txt” file after parsing it. If Amkor wishes to delete if after parsing, you can set this to TRUE
  <STDF>true</STDF>
    If this is TRUE, APL will set any STDF data from “lotinfo.txt” file into Unison so it can be set in the STDF file.
    Default is FALSE
  <Step state = "false">
    This feature is used specifically for ST/DMDx setup. In ST/DMDx setup, “lotinfo.txt” file may contain a field called “STEP”.
    Default is FALSE
    If this is set to TRUE, APL will add MIR.FLOW_ID, MIR.RTST_COD and MIR.CMOD_COD to “lotinfo.txt” based on STEP value from “lotinfo.txt” file.; if any of these fields already exists in “lotinfo.txt” file, APL will modify their values instead.
  </Field>
    This tag allows you to configure how APL will map STDF fields into “lotinfo.txt” file.

## Slide 22: Configuration File: LotInfo <Step>
On ST/DMDx setup, “lotinfo.txt” may contain a field called “STEP”. It’s value will refer to matching values for MIR.RTST_COD, MIR.FLOW_ID, and MIR.CMOD_COD
Mapping is set through config.xml and below is an example
  <Step state = “true">
  <Param flow_id = "FT1" rtst_cod = "0“ cmod_cod = “F”>fT1</Param>
  <Param flow_id = "FT1" rtst_cod = "1“cmod_cod = “F”>RT1</Param>
  </Step>
In the above example, if STEP: FT1 in “lotinfo.txt” file, MIR.FLOW_ID will be set to “FT1”, MIR.RTST_COD to “1” and MIR.CMOD_COD tp “F”
In future, Amkor may want to add more combinations for STEP so you can add it here

## Slide 23: Configuration File: LotInfo <Field>
The field/value pair labels contained in “lotinfo.txt” file can be customized
An example is MIR.LOT_ID field. if customer/amkor wants APL to set MIR.LOT_ID, it can specify any field as MIR.LOT_ID in lotinfo.txt file. Let’s say Amkor wants to call MIR.LOT_ID as “MyLotId” so it will set this in “lotinfo.txt” file as
  MyLotId: LOTABCXYZ
    Where “LOTABCXYZ” is LOT ID
  In order for APL to recognize field “MyLotId” as MIR.LOT_ID, it has to be configured in <Field> tag
  Below is an example
  <LotInfo>
  <Field>
  <Param name = "LOT_ID">MyLotId</Param>
  <Param name = "PART_TYP">MyPartType</Param>
  </Field>
  </LotInfo>
Some fields that are not STDF can also be customized. “JOBFILE” field which refers to the program name/path for which APL is supposed to load in Unison can be customized as shown below
  <Param name = “JOBFILE">MyProgramPath</Param>

## Slide 24: Configuration File: LotInfo <Field>
The field/value pair labels contained in “lotinfo.txt” file can be customized
An example is MIR.LOT_ID field. if customer/amkor wants APL to set MIR.LOT_ID, it can specify any field as MIR.LOT_ID in lotinfo.txt file. Let’s say Amkor wants to call MIR.LOT_ID as “MyLotId” so it will set this in “lotinfo.txt” file as
  MyLotId: LOTABCXYZ
    Where “LOTABCXYZ” is LOT ID
  In order for APL to recognize field “MyLotId” as MIR.LOT_ID, it has to be configured in <Field> tag
  Below is an example
  <LotInfo>
  <Field>
  <Param name = "LOT_ID">MyLotId</Param>
  <Param name = "PART_TYP">MyPartType</Param>
  </Field>
  </LotInfo>
Some fields that are not STDF can also be customized. “JOBFILE” field which refers to the program name/path for which APL is supposed to load in Unison can be customized as shown below
  <Param name = “JOBFILE">MyProgramPath</Param>

## Slide 25: Configuration File: LotInfo <Field> Continued…
The following are defaults mappings for <Field>
MIR Field | Default Lotinfo Field
SETUP_T | SETUP_T
START_T | START_T
STAT_NUM | STAT_NUM
MODE_COD | TESTMODE
RTST_COD | LOTSTATE
PROT_COD | PROTECTIONCODE
BURN_TIM | BURN_TIM
CMOD_COD | COMMANDMODE
LOT_ID | LOTID
PART_TYP | DEVICE
NODE_NAM | NODE_NAM
TSTR_TYP | TESTERTYPE
JOB_NAM | JOB_NAM
JOB_REV | FILENAMEREV
SBLOT_ID | SUBLOTID
OPER_NAM | OPERATOR
EXEC_TYP | SYSTEMNAME
EXEC_VER | TARGETNAME
TEST_COD | TESTPHASE
MIR Field | Default Lotinfo Field
AUX_FILE | AUXDATAFILE
PKG_TYP | PACKAGE
FAMLY_ID | PRODUCTID
DATE_COD | DATECODE
FACIL_ID | TESTFACILITY
FLOOR_ID | TESTFLOOR
PROC_ID | FABRICATIONID
OPER_FRQ | OPERFREQ
SPEC_NAM | TESTSPECNAME
SPEC_VER | TESTSPECREV
FLOW_ID | ACTIVEFLOWNAME
SETUP_ID | TESTSETUP
DSGN_REV | DESIGNREV
ENG_ID | ENGRLOTID
ROM_COD | ROMCODE
SERL_NUM | TESTERSERNUM
SUPR_NAM | SUPERVISOR
TST_TEMP | TEMPERATURE
USER_TXT | USERTEXT
SDR Field | Default Lotinfo Field
HAND_TYP | PROBERHANDLERTYPE
CARD_ID | CARDID
CARD_TYP | CARDTYPE
LOAD_ID | BOARDID
HAND_ID | PROBERHANDLERID
DIB_TYP | DIBTYPE
CABL_ID | CABLEID
CONT_TYP | CONTACTORTYPE
LOAD_TYP | BOARDTYPE
CONT_ID | CONTACTORID
LASR_TYP | LASERTYPE
LASR_ID | LASERID
EXTR_TYP | EXTRAEQUIPMENTTYPE
EXTR_ID | EXTRAEQUIPMENTID
DIB_ID | DIBID
CABL_TYP | CABLETYPE
Generic Field | Default Lotinfo Field
JOBFILE | JOBFILE
CUSTOMER | CUSTOMER
DEVICENICKNAME | DEVICENICKNAME
STEP | STEP

## Slide 26: Configuration File: Binning Parameters
<Binning> controls the feature that performs the binning solution (v1.4) for Amkor
If enabled, it will send per-site binning data every end-of-test to specified remote server IP.
This feature is enabled by default
< Binning > can contain the following tags (Note that Param name is case sensitive but the values are not)
  <BinType>soft</BinType>
    Specifies if bin information to be send is hard or soft bin.
    Set ‘hard’ for hard bin, ‘soft’ for soft bin. Default is soft bin
  <TestType>wafer</TestType>
    Specifies the test type.
    Set wafer for EWS and final for FT. default is wafer
  <SocketType>udp</SocketType>
    Specifies the socket connection type
    Set tcp for TCP-IP and udp for UDP. Default is tcp
  <IP>127.0.0.1</IP>
    Specifies the IP address of the server to send binning to
  <Port>4000</Port>
    Specifies the port in the server to send binning to

## Slide 27: Configuration File: Other Parameters
<STDF> allows APL to take STDF fields from “lotinfo.txt” and sends it to Unison to be set in STDF file
  Set to true to enable it. Enabled by default.
<FAMODULE> allows APL to pass the “lotinfo.txt” to FAModule to process it.
  Set to true to enable it. Enabled by default.
<Logging> is the logging mechanism of APL. If enabled, all the events that it performs and encounter is logged into a file
  The <Path> specifies the folder the log file is stored
  Set to true to enable it. Enabled by default

## Slide 28: Launching
To launch APL, just do the command:
  >apl_exec –tester <tester name> -config <config file/path>
  Note that the config file/path refers to the configuration file you want APL to use. It can be any filename or in any folder in the tester

## Slide 29: STDF fields: MIR
APL is able to write MIR fields into STDF; Some fields cannot be set due to restrictions from Unison.
MIR | Status |  | MIR | Status
LOTID | Can write |  | SBLOTID | Can write
CMODCOD | Can write |  | JOBNAM | read only, unison fills it with test program object name
FLOWID | Can write |  | SETUPID | Can write
DSGNREV | Can write |  | JOBREV | Can write
DATECOD | Can write |  | EXECTYP | Can write
OPERFRQ | Can write |  | EXECVER | Can write
OPERNAM | Can write |  | AUXFILE | Can write
NODENAM | can be set, but when lot starts, unison overwrites it with tester name |  | RTSTCOD | read only, unison fills it with specific single character values - N (new test), R (retest), U (unknown test)
PARTTYP | Can write |  | TESTCOD | Can write
ENGID | Can write |  | USERTXT | Can write
TSTTEMP | Can write |  | ROMCOD | Can write
FACILID | Can write |  | SERLNUM | Can write
FLOORID | Can write |  | SPECNAM | Can write
STATNUM | read only, unison fills it with test head number |  | TSTRTYP | Can write
PROCID | Can write |  | SUPRNAM | Can write
MODECOD | Can write |  | SPECVER | Can write
FAMLYID | Can write |  | PROTCOD | Can write
PKGTYP | Can write |  | BURNTIM | cannot be set

## Slide 30: STDF fields: SDR
APL is able to write SDR fields into STDF; Some fields cannot be set due to restrictions from Unison.
SDR | Status
HANDTYP | can be set, but unison will overwrite it with CURI driver name
CARDID | Can write
LOADID | Can write
HANDID | can be set, but unison will overwrite it with CURI object name
DIBTYP | Can write
CABLEID | Can write
CONTTYP | Can write
LOADTYP | Can write
CONTID | Can write
LASRTYP | Can write
LASRID | Can write
EXTRTYP | Can write
EXTRID | Can write
DIBID | Can write
CARDTYP | Can write
CABLETYP | can be set, but unison will overwrite it with empty string; strange behavior, need to raise SPR

## Slide 31: Thank You